## Slide 1
FPGA Temperature Regulation using PID Control in VHDL
David Paquette

## Slide 2
Goal
Regulate the temperature of the FPGA using on board temperature sensor and external DC fan
User selectable desired temperature
View the current and desired temperature on an external display
Collect current temperature and current fan speed on an external computer

## Slide 3
I/O Data Flow
VGA
UART
PWM
Temperature Sensor
Push Buttons
On board I/O

## Slide 4
High-Level VHDL Architecture
VGA WB
BRAM WB
Temperature Control Master
Clock Divider
Set point control
MemWrite WB
PID Control
Temp Sensor
PWM Interface
Values2
Serial
Char8x12 LUT
Dec 2ascii
OnePress
Filter
Debouncer
FPGA Monitor
UART
library

## Slide 5
Internal Data Flow

## Slide 6
Temperature Sensor Module
Used XADC temperature sensor to measure the FPGA temperature
For now, truncated temperature at 8 bits.
Can measure in 1˚C increments
FPGAMonitor
clk
rst
ADC Code
Temperature
Sensor Module
Temperature(˚C)
Analog digital converter code to temperature
Derived from
Equations found in Xilinx XADC user guide
Voltage is sampled by the 12-bit ADC to produce an ADC Code
k=Boltzmann’s constant
T = temperature (K)
q=charge on an electron

## Slide 7
Temperature Selection Module
Increment set point
Decrement set point
start
One press
No press
Btn=1
Btn=1
Btn=0
Btn=0
Outputs the user’s desired temperature
Set by using the push button pad on the FPGA
One press and debouncer state machine used
One press state machine

## Slide 8
DC Motor Control Module
Pmod digital output high is 3.3V
DC motor is controlled with 0 to 5V
DC motor functions in PWM frequency range 100Hz to 600Hz (from testing)
Wait for rising edge clock
Desired Fan Speed (%)
Increment counter
counter < (desired fan speed)
yes
no
Output = 1
Output = 0
Duty Cycle % to PWM
3.3V to 5V PWM DC Motor Driver

## Slide 9
UART Serial Module
1 http://bytebash.com/2011/10/rs232-uart-vhdl
X
0x2C
X
0x0A
Serial format used for sending data.
‘X’ is an 8-bit value (Current temperature and fan speed).
0x2C is ASCII for a comma (,)
0x0A is ASCII for a newline (\n)
UART Library
Diagram of UART library1
(only relevant ports shown)
clk
rst
dat_in[8]
stb_i
ack_o
rx
start
Send Temp
Send Comma
Send fan speed
Send newline
wait
ack_o=1
ack_o=1
ack_o=1
ack_o=1
counter=10ms
State machine for interfacing with UART library
Each state asserts the stb_i pin on entry and de-asserts it on exit.

## Slide 10
VGA BRAM Display Module
Current and desired temperature are written to BRAM over Wishbone
VGA module reads pixel data from BRAM over Wishbone
InitMem
Start
Get Pixel Data
Write to Mem
row=39
line<11
ack_i=1
Display format
cT=XX
dT=XX
BRAM Writer State Machine
Decimal to two digit ASCII conversion

## Slide 11
Digital PID Controller Module
Wait for rising edge clock
e =desiredT – currentT
sum += e
changeE = e -previousE
newFanSpeed = Kp*e+Ki*e*T+Kd*changeE/T
Simplified PID control
Added windup protection to prevent integral term from becoming too large
Added output bounds checking to prevent fan speed from being set over 100% or under 0%
= measured temperature
= desired temperature
= fan speed
= 10ms
Safety Checks

## Slide 12
System Identification
Set fan to 60% after 5 seconds and
Captured temperature data through serial port
Used the system identification tool box in MATLAB to estimate the discrete open loop transfer function
Sampling rate of 10ms
Open loop unit step response (no control)
Open loop transfer function

## Slide 13
Controller Design and Results
Used MATLAB’s PID toolbox to estimate closed loop gains
Tested gains on FPGA (worked well)
Settling time of about 15 seconds
To avoid using decimals, Kp and Ki are set as 303 and 123, then the controller output is divided by 100
Closed loop response
Set point=34
Set point=32

## Slide 14
Implemented Circuit and Display
Completed PWM DC motor driver circuit
VGA display format

## Slide 15
Remaining Work
Add module to generate heat, for testing controller response under varying conditions
Limit desired temperature to reasonable range
Display fan speed on VGA
Move communication between fan, PID controller, temperature sensor, buttons and serial port to wishbone bus

## Slide 16
Questions